CflexHDL
Design digital circuits in C
        Simulate really fast with a regular compiler
© Victor Suarez Rovere

---
Language benefits
- C is much more known than
  Verilog/VHDL
- Helps to break the "scary" barrier to enter circuit design by embedded software developers
- Automatic FSMs from control flow ("while loops")
- Comfortable debugging (tools new and upcoming like gdbwave)

---
Simulation speed benefits
- Running compiled C code is even
  faster than fast HDL simulators
- Simulator runs at 220MHz clock speed (LED glow demo)
- The 3D-like video demo surpasses realtime, even with a 15 years old CPU: 126FPS - 38M pixel/s
- Original demo: 0.82 FPS (156X slower) - Silice’s “make verilator”

---
Development time benefits
- Compiling C is much faster than doing synthesis (seconds instead of minutes)
- 240X to 1028X faster than common
  synthesis toolchains (led glow demo)
- Notable exception: Yosys + NextPNR (just 67X slower)

---
Led glow demo
Argument led represents
the output pin
Bit range access using C
Bitfields, and a union for aliasing
When not translated to verilog,
the always() function defers
execution to the simulator
Sets bit output
and updates register.
The function never returns

---
Synthesis Workflow
.cc file
C parsing
.ice file
Silice
generated
source
.v file
Verilog
source
Migen /
LiteX
integration
  Bitstream
Synth
& load
The C files are translated to verilog and integrated into existing toolchains

---
Development innovations
- The tool is novel in itself, but also required the development of non-existing modules such as:
  - CflexParser: the first C++ parser/generator for python. Based on clang indexer’s bindings (tool to be released stand-alone)
  - Adding previously unsupported boards to Silice projects
  - Graphic display on the simulator: running the original C code or the Verilator output using a same codebase
  - Integration of Yosys+NextPNR into LiteX framework: mainlined

---
Ease of running & testing
- Compile project (for simulation) or synth the bitstream and load, using just make
- Currently supporting:
  - Digilent Arty A7 board (Xilinx Artix-7)
  - Terasic DE0-Nano (Intel Cyclone IV)
  - All boards supported by LiteX, easy to add

---
3D-like video generation demo
- A VGA demo* was manually ported to C
- CflexHDL runs the C logic using any of:
  - A simulator that opens a window, after compiling the C sources in 1.3 seconds
  - A FPGA board with analog or digital video output (automatically generates and loads the bitstream)
  - Verilator output on the simulator window (same graphics but at lower FPS)
* https://github.com/sylefeb/Silice/blob/master/projects/vga_demo/vga_flyover3d.ice

---
Example C & generated code (FSM)

---
It works! (TM)
$ cd demos/vga
$ make load run
  - Makes bitstream,
  - loads it,
  - compiles the C source,
  - and runs it in the simulator window

---
Dependencies
- Sylvain Lefebvre’s Silice HDL: https://github.com/sylefeb/Silice
- Clang’s indexer bindings: https://pypi.org/project/clang/
- Enjoy Digital’s LiteX: https://github.com/enjoy-digital/litex
- Open FPGA Loader: https://github.com/trabucayre/openFPGALoader
- SDL 2: https://www.libsdl.org
- GNU gcc or Clang
- Python 3.x

---
Planned improvements
- Remove depedency with Silice HDL (needs
  to add FSM logic generation)
- Adopt some C++ syntax like templates to access bit fields
- Port a C soft-float library to support floating point in the FPGA
- Integrate the soon to be released CflexTypes library, currently providing:
  - Integer, fixed point and floating point types of variable widths
  - Instrumented templates with operator overloading, for benchmarking resource usage at simulation time and effect of varying bit widths (already tested)

---
Thanks!
https://github.com/suarezvictor/CflexHDL/